## Slide 1
COMPUTER VISION (20XW97) · COURSE PRESENTATION
Computer Vision & Automation
From pixels to penalties: automated speed enforcement on Coimbatore's GD Naidu Flyover
Thithiksha · Arul · DPD
60
km/h · posted limit on the flyover
Notes: [Thithiksha | ~30 s] Good morning. We're Thithiksha, Arul and DPD, and our topic is Computer Vision and Automation. Rather than survey the field, we'll take one real, local problem and build the whole solution in front of you: detecting speeding vehicles on Coimbatore's GD Naidu Flyover using only a camera. The 60 on this slide is the flyover's posted speed limit. Everything in the next 25 minutes builds towards one question: did a vehicle cross 60, and can a computer decide that by itself? I'll cover how machines see, Arul will explain how we go from detections to speed, and DPD will close the loop and run a live demo.

## Slide 2: Tamil Nadu's longest flyover has a speeding problem
THE PROBLEM
Uppilipalayam
Goldwins
Elevated over Avinashi Road · 4 lanes · bypasses ~12 junctions (dashed)
10.1 km
Tamil Nadu's longest flyover, opened 9 Oct 2025
60 km/h
Posted speed limit on the elevated corridor
3 killed
Car off the flyover hit a parked truck near Goldwins, days after opening
Why it matters: on a long, uninterrupted, elevated stretch, drivers misjudge speed. Police say the flyover tempts drivers well past 60 km/h.
Sources: Wikipedia, G. D. Naidu Elevated Expressway; The Week (9 Oct 2025); Lokmat Times; BizzBuzz.
Notes: [Thithiksha | ~1 min] This is the GD Naidu Elevated Expressway on Avinashi Road: 10.1 kilometres, four lanes, from Uppilipalayam to Goldwins. It opened on 9 October 2025 and it's the longest flyover in Tamil Nadu. It skips about twelve signals, which is exactly why people speed on it. The posted limit is 60 km/h. Within days of opening, a car coming off the flyover near Goldwins hit a parked truck and three people died. Witnesses said vehicles routinely ignore the limit. On an elevated road with no junctions, you lose your sense of speed, so 90 can feel like 60. A traffic officer with a radar gun can't cover 10 km. That's an automation problem, and the sensor that can solve it is a camera.

## Slide 3: AI enforcement is already installed here, and still in trial
REALITY CHECK
44
AI-enabled cameras along the flyover
16
digital display boards
₹3 Cr
approximate project cost
3+ months
in trial, no fines issued
Reported system accuracy during trial
Early trial
20%
After tuning
80%
Problems reported: misidentified violations, e.g. seat-belt detection errors
Today's question: how does such a system work, and why isn't 80% good enough to fine people?
Sources: BizzBuzz; The Hawk; NewKerala (2026) on the GD Naidu Flyover AI speed-enforcement trial.
Notes: [Thithiksha | ~1 min] This isn't hypothetical. The State Highways Department has installed 44 AI cameras and 16 display boards on this flyover, for about 3 crore rupees. More than three months after installation, the system was still in trial and no fines had been issued. The reason was accuracy: it reportedly started at around 20%, with misidentified violations, and was tuned up to about 80%. 80% sounds good until you remember that one in five tickets would go to the wrong person. That's the tension in this whole talk: automating perception is easy to demo and hard to trust. So today we'll show how a system like this works, stage by stage, where it breaks, and then a working version of it.

## Slide 4: One pipeline, five stages, three speakers
ROADMAP
PIXELS
Image as numbers
DETECT
Find vehicles (YOLO)
TRACK
Keep identity (ByteTrack)
MEASURE
Pixels → metres → km/h
ACT
Rule → evidence → alert
01 Thithiksha
How machines see
~7 min
02 Arul
From detections to speed
~8 min
03 DPD
Automation + demo
~6 min + demo
Notes: [Thithiksha | ~40 s] Here's the map for the talk. Every automated vision system is a pipeline, and ours has five stages. Pixels: what an image actually is to a computer. Detect: finding every vehicle in a frame. Track: knowing that the car in this frame is the same car in the next frame. Measure: converting pixel movement into kilometres per hour. Act: turning that number into a decision and evidence, with no human in between. I'll cover pixels and detection. Arul, who built this system during his internship, covers tracking and measurement. DPD closes the loop with automation and the live demo. Watch the small chips at the top right of each slide; they show where we are in the pipeline.

## Slide 5: How machines see
01
Thithiksha · Pixels and detection
PIXELS
DETECT
TRACK
MEASURE
ACT
Notes: [Thithiksha | ~10 s] Let's start at the bottom: what does a camera actually give a computer?

## Slide 6: To a computer, an image is just a grid of numbers
PIXELS
PIXELS
DETECT
TRACK
MEASURE
ACT
[ image: pixels.png ]
1920 × 1080 × 3
≈ 6.2 million numbers in one 1080p colour frame
× 30 FPS
≈ 187 million numbers every second
0 – 255
intensity per channel (R, G, B)
Every CV task turns this array into a decision.
Notes: [Thithiksha | ~1 min] A camera doesn't give us "a car". It gives us a 3D array: height, width, and three colour channels, each value from 0 to 255. On the left is a frame from highway footage, and the zoom shows the actual pixel values around one vehicle. One 1080p frame is about 6.2 million numbers. At 30 frames per second, that's nearly 190 million numbers every second. Everything in computer vision, whether it's classical image processing or deep learning, is a function that takes this array and produces something useful: a mask, a box, a label, or here, a speed. The rest of the talk is that function, one stage at a time.

## Slide 7: Classical CV sees motion, not vehicles
CLASSICAL CV
PIXELS
DETECT
TRACK
MEASURE
ACT
[ image: background_subtraction.png ]
How it works: model the static road (MOG2 background model); pixels that differ from it are 'foreground'.
Where it breaks
Shadows move with the car → oversized blobs
Headlights & night glare → false motion
Camera shake on a flyover → whole frame 'moves'
Two close cars merge into one blob
No labels: car, bus or bike?
Fast, no training, too fragile for fines
Notes: [Thithiksha | ~1.5 min] Before deep learning, the standard approach to traffic video was background subtraction. You build a statistical model of the empty road (OpenCV's MOG2 is a common choice), and any pixel that differs from it is marked as foreground. On the right of the image you see the mask: white blobs where things are moving. It's fast and needs no training data, but look at the failure list. Shadows move with the vehicle and inflate the blob. At night, headlight glare creates motion where there's no car. A flyover vibrates, so the whole frame can look like it's moving. Two cars close together merge into one blob. And it never tells you what the blob is. For counting traffic it's often fine; for issuing a fine to a specific vehicle it isn't. We need a method that recognises vehicles, not just motion.

## Slide 8: CNNs learn their own feature detectors from data
DEEP LEARNING
PIXELS
DETECT
TRACK
MEASURE
ACT
Convolution: slide a small kernel over the image, multiply and sum at each position. High output = the pattern is present here.
Early layers
edges, corners, colour blobs
Middle layers
parts: wheels, windows, plates
Deep layers
whole objects: car, bus, truck
Kernels are learned by training, not hand-written. YOLOv8 is pre-trained on COCO: 118k images, 80 classes.
Notes: [Thithiksha | ~1.5 min] Convolutional neural networks fix this by learning what to look for. The core operation is convolution: take a small grid of weights called a kernel, slide it across the image, and at every position multiply and add. In the animation the kernel is a Sobel filter, and the output lights up exactly where dark meets bright: a vertical edge. The key difference from classical CV is that a CNN learns thousands of these kernels from data instead of us designing them. Stacked in layers, early kernels find edges, middle layers combine them into parts like wheels and windows, and deep layers respond to whole objects. We don't train from scratch. YOLOv8 comes pre-trained on COCO, 118 thousand images with 80 classes, and those classes already include car, motorcycle, bus and truck. That's why our demo needed no training at all.

## Slide 9: YOLO finds every vehicle in a single pass
OBJECT DETECTION
PIXELS
DETECT
TRACK
MEASURE
ACT
[ image: frame_detections.png ]
1
Grid
Image split into cells at 3 scales; each cell predicts boxes
2
Predict
Per box: x, y, w, h + class scores (car 0.91)
3
NMS
Keep the best box, drop overlapping duplicates (IoU > threshold)
3.2 M
parameters
37.3
mAP COCO
8.7 G
FLOPs
YOLOv8n (nano), as used in our demo. Source: Ultralytics docs.
Notes: [Thithiksha | ~1.5 min] Object detection answers two questions at once: what is in the image, and where. The output is a bounding box, a class and a confidence score, like the boxes on this frame. YOLO, "You Only Look Once", does it in a single forward pass of the network. The image is divided into grid cells at three scales. Each cell predicts box coordinates and class scores. That produces many overlapping candidate boxes for the same car, so a final step called non-maximum suppression keeps the highest-confidence box and removes others that overlap it too much. We use YOLOv8 nano, the smallest model: 3.2 million parameters, 37.3 mAP on COCO, small enough to run on a laptop CPU. That trade-off between size and accuracy comes back in DPD's section.

## Slide 10: Detectors are scored on overlap, not 'accuracy'
EVALUATION
PIXELS
DETECT
TRACK
MEASURE
ACT
Ground truth
Prediction
IoU = overlap ÷ union
IoU ≥ 0.5 → counts as a correct detection (true positive)
Precision
TP ÷ (TP + FP)
Of vehicles flagged, how many were real?
Recall
TP ÷ (TP + FN)
Of the real vehicles, how many did we catch?
mAP
avg AP · IoU 0.5–0.95
Single quality score: 37.3 for YOLOv8n
For enforcement, precision comes first: every false positive is an innocent driver fined.
Notes: [Thithiksha | ~1.5 min] How do we know a detector is good? Not with a single "accuracy" number. First, a predicted box only counts as correct if it overlaps the true box enough. That's Intersection over Union: overlap area divided by combined area. The usual threshold is 0.5. Then two numbers. Precision: of everything we flagged, how much was real? Recall: of everything that was really there, how much did we find? mAP averages precision across classes and across IoU thresholds from 0.5 to 0.95. That's the 37.3 on the previous slide. For speed enforcement these aren't equally important. Missing a speeder (low recall) means one gets away. A false positive (low precision) means an innocent person gets a fine. That's why the flyover system stayed in trial at 80%. That's detection. Over to Arul, who'll show why detection alone can't measure speed.

## Slide 11: From detections to speed
02
Arul · Tracking and measurement
PIXELS
DETECT
TRACK
MEASURE
ACT
Notes: [Arul | ~10 s] Thanks, Thithiksha. We can now find vehicles in a frame. To measure speed we need two more things: memory and a ruler.

## Slide 12: Detection has no memory; tracking adds identity
WHY TRACKING
PIXELS
DETECT
TRACK
MEASURE
ACT
Detection only
car
t
car
t + 1
car
t + 2
Same car? Unknown. No speed possible.
With tracking
#7
t
#7
t + 1
#7
t + 2
One identity → a trajectory → a speed.
Notes: [Arul | ~1 min] YOLO processes every frame independently. In frame t it says "car", in t+1 "car", in t+2 "car". It has no idea these are the same car, and speed is about the same object moving over time. So we add tracking: give every vehicle a persistent ID, here number 7, and follow it from frame to frame. Once we have an identity, we have a trajectory, a list of positions over time. A trajectory plus a clock gives us speed. The tricky part is that tracking has to survive the real world: missed detections, cars hidden behind trucks, and many similar-looking cars side by side.

## Slide 13: ByteTrack: predict, match, then rescue weak boxes
MULTI-OBJECT TRACKING
PIXELS
DETECT
TRACK
MEASURE
ACT
Predict
Kalman filter estimates each track's next box from its velocity
Match
High-confidence boxes ↔ predictions by IoU (Hungarian assignment)
Rescue
Low-confidence boxes matched to leftover tracks: keeps occluded cars
Update
Unmatched boxes → new IDs; tracks lost ~1 s → deleted
↻ repeats every frame
[ image: tracking_preview.gif ]
80.3
MOTA
77.3
IDF1
30 FPS
on MOT17
Notes: [Arul | ~2 min] We use ByteTrack, a tracker published at ECCV 2022. Every frame it runs four steps. Predict: each existing track has a Kalman filter, a constant-velocity motion model, that predicts where its box should be in the new frame. Match: we compare those predictions with YOLO's high-confidence detections using IoU, and the Hungarian algorithm finds the best one-to-one assignment. Rescue: this is ByteTrack's key idea. Most trackers throw away low-confidence detections. ByteTrack does a second matching round with them against the tracks that are still unmatched. A car half-hidden behind a bus gets a low score but it's still a real car, so its ID survives. Update: leftover detections start new tracks, and tracks unseen for about a second are deleted. On the MOT17 benchmark it reports 80.3 MOTA at 30 frames per second. In code it's one line from the supervision library.

## Slide 14: A homography turns pixels into metres
CAMERA GEOMETRY
PIXELS
DETECT
TRACK
MEASURE
ACT
[ image: homography_before.png ]
[ image: homography_after.png ]
Camera view: 4 points on the road
Bird's-eye view (metres)
The problem
Perspective shrinks distance: 1 m near the camera spans many more pixels than 1 m far away.
The fix
Map 4 road points to a rectangle of known size. 4 point pairs → 8 equations → the 3×3 matrix H.
p′ ∝ H · p
p = [x, y, 1]ᵀ (homogeneous)
Zone calibrated from lane markings (assumed lane width).
Notes: [Arul | ~1.5 min] Now we can follow a car in pixels, but speed needs metres. The camera's perspective is the problem: a car near the camera moves many pixels per metre, and a car far away moves only a few. The same speed would look different depending on where the car is. The fix is a homography: a 3×3 matrix that maps one plane to another. We click four points on the road that form a rectangle in the real world, for example lane markings, and tell the computer the real width and length of that rectangle in metres. Four point pairs give eight equations, enough to solve for H. OpenCV does this with getPerspectiveTransform. Apply H to every car's position and we get the bird's-eye view on the right, where one unit is one metre everywhere. For our footage the real size comes from standard lane widths; on the real flyover you'd measure it on site.

## Slide 15: Speed is metres travelled per second of video
SPEED ESTIMATION
PIXELS
DETECT
TRACK
MEASURE
ACT
v = |Δy| ÷ (N ÷ FPS) × 3.6
Δy: metres moved in the bird's-eye view
N: frames in the window (~1 s)
× 3.6: m/s → km/h
Worked example from our demo · track #—
— m
distance in zone
— frames
at — FPS = — s
— m/s
Δy ÷ time
— km/h
vs 60 km/h limit
Why a 1-second window? A single frame-to-frame step is a few cm and dominated by box jitter; averaging over ~30 frames gives a stable reading.
Notes: [Arul | ~1.5 min] With metres and a clock, speed is simple arithmetic. For each tracked vehicle we keep its position in the bird's-eye view over the last second of frames. Speed is the distance it moved divided by the time, and the time is the number of frames divided by the frame rate. Multiply metres per second by 3.6 to get kilometres per hour. Here's a real vehicle from our run: it moved Δy metres over N frames. Why one second and not frame to frame? Between two consecutive frames a car moves maybe 50 centimetres, and the box edge wobbles by a similar amount. Averaging over about thirty frames smooths that out. The cost is that a new vehicle needs about half a second before we trust its speed.

## Slide 16: Small measurement errors become wrong fines
ERROR ANALYSIS
PIXELS
DETECT
TRACK
MEASURE
ACT
What the system reads for a car truly doing 60 km/h
Chart: 
| No error | Box jitter ±0.5 m | Zone length 4% off | FPS assumed 30, really 25
Reading (km/h) | 60 | 61.8 | 62.4 | 72
Above 60 → flagged. Every non-zero error here would fine a legal driver.
Mitigations
Survey the calibration zone on site, not from assumptions
Read real frame timestamps; never assume FPS
Median over a window; drop ID-switched tracks
Enforcement tolerance, e.g. flag only above limit + margin
Notes: [Arul | ~1.5 min] This is where it's easy to oversell, so let's be precise. Speed equals distance over time, so any error in distance or time goes straight into the speed. Box jitter of half a metre over one second adds about 1.8 km/h. If the calibration zone is 4% off, say 52 metres assumed when it's really 50, every speed is 4% high and a car at 60 reads 62.4. The worst is time: if the code assumes 30 frames per second and the camera actually records 25, every speed is 20% high, and a legal driver at 60 shows as 72. Every one of these would fine someone who did nothing wrong. So we calibrate on site, read real timestamps, use the median over a window, drop tracks whose ID switched, and real systems add an enforcement tolerance above the limit. That's tracking and measurement. DPD will now close the loop.

## Slide 17: Closing the loop
03
DPD · Automation, deployment and live demo
PIXELS
DETECT
TRACK
MEASURE
ACT
Notes: [DPD | ~10 s] Thanks, Arul. We now have a number, a speed in km/h. Automation is what happens next, without a human in the loop.

## Slide 18: Automation turns a measurement into an action
AUTOMATION
PIXELS
DETECT
TRACK
MEASURE
ACT
Measure
Speed per track
Decide
v > 60 km/h ?
Evidence
Snapshot: box, ID, speed, time
Record
Append to violations log
Act
Alert / display board / e-challan
In our demo
Rule check every frame
Red box + live counter
Evidence JPEG
CSV violation log
A production system adds
Number-plate reading
Human review of every case
e-challan integration
Display-board warnings
Notes: [DPD | ~1.5 min] Classic automation is sense, think, act. Vision is the sensing; this slide is the thinking and acting. For every tracked vehicle, every frame, a simple rule runs: is the speed above 60? If yes, we capture evidence: a snapshot with the box, the ID, the measured speed and the timestamp. We record it in a log, and then something acts on it: an alert, a "slow down" message on one of the flyover's display boards, or in a full system an e-challan. I want to be clear about scope. Our demo does the green column: the rule, the red box, the evidence images and the CSV log. A production system adds number-plate reading, a human reviewing every case before a fine is issued, and integration with the e-challan system. The human review is not optional. It's the answer to the 80% problem.

## Slide 19: The whole system is five open-source blocks
SYSTEM ARCHITECTURE
PIXELS
DETECT
TRACK
MEASURE
ACT
Camera
video frames
OpenCV
1080p
Detect
YOLOv8n
Ultralytics
— ms
Track
ByteTrack
supervision
— ms
Measure
Homography
OpenCV / NumPy
— ms
Act
Rule engine
Python
< 1 ms
Orange: measured time per frame on a laptop CPU
Live overlay
boxes, IDs, km/h, HUD
Evidence
one JPEG per violator
Logs
vehicles.csv · violations.csv
Notes: [DPD | ~1 min] Here's the full system as it runs in the demo. Frames come from the camera or a video file through OpenCV. YOLOv8 nano detects vehicles, ByteTrack from the supervision library assigns IDs, the homography and speed module converts positions to km/h, and the rule engine decides and records. The orange numbers are what we measured per frame on a laptop CPU. Detection is by far the most expensive stage; everything after it is almost free. That matters for the next slide. The outputs are a live annotated view, one evidence image per violating vehicle, and two CSV logs. Every block is open source, and the whole pipeline is about 200 lines of Python.

## Slide 20: Real time means a 33 ms budget per frame
DEPLOYMENT
33 ms
per frame at 30 FPS: detect + track + measure + act
— FPS
measured end-to-end in our demo on a laptop CPU
YOLOv8 size vs CPU speed (640 px)
Chart: 
| v8n · mAP 37.3 | v8s · mAP 44.9 | v8m · mAP 50.2
CPU ms / image | 80.4 | 128.4 | 234.7
Ultralytics benchmark: CPU ONNX, per image. Bigger = more accurate, slower.
Levers to fit the budget
Smallest model that's accurate enough
Lower input resolution
Process every 2nd frame (speed still works)
Edge GPU, e.g. NVIDIA Jetson
INT8 quantisation / TensorRT
Notes: [DPD | ~1 min] At 30 frames per second, everything has to finish in 33 milliseconds per frame, or the system falls behind the camera. On our machine we measured — frames per second end to end. The chart is the core trade-off, from Ultralytics' own benchmarks on CPU: the nano model takes about 80 ms per image at 37.3 mAP; the medium model is three times slower for about 13 points more mAP. For speed estimation, nano is accurate enough on cars, which are large, distinct objects. If you need more headroom: use a smaller input, process every second frame (speed is computed over a one-second window, so that still works), move to an edge GPU like a Jetson, or quantise the model to 8-bit integers.

## Slide 21: What this system cannot (yet) do
LIMITATIONS & ETHICS
Environment
Night, rain, glare and headlights reduce detection confidence; COCO is mostly daylight imagery.
Geometry
Flyover vibration and camera drift break calibration; curves and slopes violate the flat-road assumption.
Legal grade
Fines need certified, audited accuracy. The flyover trial (20% → 80%) shows how high that bar is.
Privacy
Vehicle images and plates are personal data: retention limits, access control, purpose limitation.
Notes: [DPD | ~1 min] Four limits we want to state honestly. Environment: our model was trained mostly on daylight images. Night, rain and headlight glare all reduce confidence. Geometry: a flyover vibrates, and a camera that shifts by a few pixels breaks the calibration. Our method also assumes a flat road, and real roads curve and slope. Legal grade: a demo isn't evidence. Fines require certified, audited accuracy. The real system on this flyover spent months in trial for exactly this reason. Privacy: images of vehicles and number plates are personal data, so storing them needs limits on retention, access and purpose. Now, let's see it run.

## Slide 22: Speed check demo
LIVE
YOLOv8n + ByteTrack + homography · limit 60 km/h
Watch for 1
IDs stay stable
as cars pass each other
Watch for 2
Speed settles
after ~0.5 s of tracking
Watch for 3
Red box + snapshot
the moment v > 60 km/h
Notes: [DPD | 5-10 min | DEMO CHECKLIST] BEFORE THE TALK - cd cv-automation-ppt/demo, then activate the venv - Dry run: python speed_detection.py --source <video> --show - Close other heavy apps; plug in the charger (CPU speed drops on battery) - Keep outputs/annotated.mp4 open in a video player as a BACKUP if live inference fails DURING THE DEMO (switch from PowerPoint with Alt+Tab; notes stay in Presenter View) 1. Show calibrate.py's frame with the 4-point zone: "this is the homography from Arul's slide" 2. Run live with --show. Point out: HUD (FPS, vehicles, violations), stable IDs, speed appearing after ~0.5 s 3. Pause on a red box: speed > 60, so an evidence snapshot was saved 4. Open outputs/violations/ and show one JPEG, then violations.csv 5. Optional: re-run with --limit 80 to show the rule is just a parameter SAY "Everything you just saw is the five stages from the roadmap, about 200 lines of Python, no training." Then return to PowerPoint, next slide: Results.

## Slide 23: Results
RESULTS
—
vehicles tracked
— km/h
median speed
—
flagged above 60 km/h
— FPS
processing speed (CPU)
Speed distribution of tracked vehicles
Chart: km/h
| —
≤ 60 km/h | 0
> 60 km/h | 0
Auto-captured evidence
[ image: violation_example.png ]
Footage and calibration: see demo README.
Notes: [DPD | ~1.5 min] Summarise the numbers on this slide. Two honest caveats. First, this is public highway footage, not the flyover, and the calibration uses assumed lane dimensions, so treat the absolute speeds as estimates. Second, we haven't measured ground-truth speeds with a radar, so this shows the pipeline works, not that it's certified-accurate. That validation is exactly what the real flyover system has been doing during its trial.

## Slide 24: Three things to remember
TAKEAWAYS
01
Automation = perception + measurement + rule
Detect, track, calibrate, decide: each a well-understood, open-source block. No training needed for vehicles.
02
The model is the easy part
Calibration, frame timing, night, rain and vibration decide whether the number is right.
03
Precision before scale
A false positive fines an innocent driver. Keep a human in the loop until accuracy is proven.
Notes: [DPD | ~45 s] Three things to take away. One: an automated vision system is a pipeline of perception, measurement and a rule. Each stage is well understood and available as open source; we didn't train anything. Two: the model is the easy part. Whether the speed is right depends on calibration, frame timing and conditions like night, rain and vibration. Three: precision before scale. When the output is a fine, a false positive punishes an innocent person, so keep a human in the loop until the system has proven its accuracy, as the flyover trial is doing right now.

## Slide 25: Sources
REFERENCES
Jocher, G. et al. Ultralytics YOLOv8 (2023), docs.ultralytics.com: model benchmarks (mAP, params, CPU latency)
Zhang, Y. et al. ByteTrack: Multi-Object Tracking by Associating Every Detection Box. ECCV 2022
Lin, T.-Y. et al. Microsoft COCO: Common Objects in Context. ECCV 2014
Redmon, J. et al. You Only Look Once: Unified, Real-Time Object Detection. CVPR 2016
Hartley, R. & Zisserman, A. Multiple View Geometry in Computer Vision, 2nd ed. (homography, DLT)
Zivkovic, Z. Improved adaptive Gaussian mixture model for background subtraction (MOG2). ICPR 2004
Roboflow supervision: speed-estimation example (YOLO + ByteTrack + perspective transform), github.com/roboflow/supervision
Wikipedia: G. D. Naidu Elevated Expressway; The Week, 9 Oct 2025: Tamil Nadu's longest flyover opened
Lokmat Times: three killed after car hits parked truck near GD Naidu Flyover
BizzBuzz; The Hawk; NewKerala (2026): Coimbatore flyover AI speed cameras remain under trial
Notes: Reference slide. No need to read out; leave up briefly if asked about sources.

## Slide 26
Thank you
Questions?
Thithiksha · Arul · DPD
Computer Vision (20XW97)
60
Notes: [DPD] Thank you. We're happy to take questions, on the theory or on the code. Likely questions: - Why not radar? Radar is accurate but per-lane and expensive; one camera covers several lanes and also gives evidence images. Real systems often fuse both. - How accurate is it? Without radar ground truth we can't claim a number. The error analysis slide shows how to bound it. - Number plates? Needs a higher-resolution camera and an OCR stage (for example a plate detector followed by an OCR model). That's the next extension. - Night? Needs IR illumination or a model fine-tuned on night footage.